# New allround device for resistance measurement leaves nothing to be desired

Resistance measurement and RESISTOMAT® are both terms that indispensably belong together. burster presents with its newly developed and good value RESISTOMAT® 2316 a tough, universal and compact resistance measurement device that suits to applications in rough industry surroundings as well as in fair laboratory conditions. 40 years of know how and experience in the field of resistance measurement flew into the development of this measurement device that combines precision as well as easy handling and system integration capability quite perfectly.

The instrument measures resistances in the range of 2,0000 mΩ up to 200,00 kΩ with an accuracy of 0.03 % rdg., whereat the resolution in the smallest range reaches 0.1 μΩ. An especially developed measurement input protection allows particularly the measurement of inductive samples as i.e. electric motors and transformers as much as coils with iron core. The measurement of heating elements, fuses, switch and relay contacts or cables and wires are only a few further application fields.

Autorange, temperature compensation of the test sample, cable fraction detection and thermovoltage compensation are self-evident. For the integration into fully automatic test stations the instrument features a PLC and RS232/USB interface.

Thanks to the large and backlit LCD display the measuring value can be easily read off also from a major distance in dim production halls as well as in face of direct solar radiation. The simply designed choice of the different measuring parameters is effected via an elaborate operation menu that provides 5 languages English, French, Spanish, Italian and German.

# Press Release No. 501

Words: 249

Lines: 18

Product Responsibility:	Edgar Bender			Phone: +49-7224-645-19

Marketing / Media:		Christina Strohm		Phone: +49-7224-645-85